## Slide 1: SWITCHING THEORY AND LOGIC DESIGN
UNIT-3
BY
S.SAGAR KRISHNA,
ASSISTANT PROFESSOR,
GAYATRI VIDYA PARISHAD COLLEG OF ENGINEERIN(A)

## Slide 2: BCD TO EXCESS-3 CONVERTER
Procedure:
Write the functional table.
Using K-MAP get the Boolean expressions for each output.
Draw the logic diagram.

## Slide 3: BCD TO EXCESS-3 CONVERTER
Functional Table:

## Slide 4: BCD TO EXCESS-3 CONVERTER
Boolean expressions for each output:

## Slide 5: BCD TO EXCESS-3 CONVERTER
logic diagram :

## Slide 6: Decoders
A decoder has
  N inputs
  2N outputs
A decoder selects one of 2N outputs by decoding the binary value on the N inputs.
The decoder generates all of the minterms of the N input variables.
  Exactly one output will be active for each combination of the inputs.

## Slide 7: 2x4 Decoder:
Logic Diagram
Functional Table of 2x4 Decoder

## Slide 8: 2x4 decoder with enable:
Inputs | Outputs
EN I1 I0 | Y3 Y2 Y1 Y0
0 X X 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0
Logic Diagram
Functional Table

## Slide 9: 3x8 decoder using 2x4 decoder
The inputs A0 and A1 is connected as parallel inputs for both the decoders and then the Enable pin of the Second Decoder is made to act as A2 (third input).
The Inverted signal of A2 is given to the Enable pin of first decoder to get the outputs Y0 to Y3. Here the outputs Y0 to Y3 is referred as Lower four minterms and the outputs Y4 to Y7 is referred as higher four minterms.
The lower order minterms are obtained from the first decoder and the higher order minterms are obtained from the second decoder.
Logic Diagram

## Slide 10: 4x16 decoder using 3x8 decoder

## Slide 11: 2x4 decoder with active low output

## Slide 12: Encoders
An encoder has
  2N inputs
  N outputs
An encoder outputs the binary value of the selected (or active) input.
An encoder performs the inverse operation of a decoder.
The encoder can be implemented with OR gates whose inputs are determined directly from the truth table. Output z is equal to 1 when the input octal digit is 1, 3, 5,or 7. Output y is 1 for octal digits 2, 3, 6, or 7, and output x is 1 for digits 4, 5, 6, or 7.

## Slide 13: Octal to Binary Encoder
Output z is equal to 1 when the input octal digit is 1, 3, 5,or 7. Output y is 1 for octal digits 2, 3, 6, or 7, and output x is 1 for digits 4, 5, 6, or 7.
Issues
  What if more than one input is active?
  What if no inputs are active?

## Slide 14: Priority Encoders
If more than one input is active, the higher-order input has priority over the lower-order input.
  The higher value is encoded on the output
A valid indicator, v, is included to indicate whether or not the output is valid.
  Output is invalid when no inputs are active
    v = 0
  Output is valid when at least one input is active
    v = 1

## Slide 15: Priority Encoders
Boolean Expressions
Logic Diagram

## Slide 16: Multiplexers
A multiplexer has
  N control inputs(Select lines)
  2N data inputs
  1 output
A multiplexer routes (or connects) the selected data input to the output.
  The value of the control inputs determines the data input that is selected.

## Slide 17: Multiplexers
Z = A′.I0 + A.I1
Data
inputs
Control
input

## Slide 18: Multiplexers
Z = A′.B'.I0 + A'.B.I1 + A.B'.I2 + A.B.I3
A | B | F
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
MSB
LSB

## Slide 19: Multiplexers
Z = A′.B'.C'.I0 + A'.B'.C.I1 + A'.B.C'.I2 + A'.B.C.I3 +
A.B'.C'.I0 + A.B'.C.I1 + A'.B.C'.I2 + A.B.C.I3
MSB
LSB
A | B | C | F
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7

## Slide 20: Multiplexers
Logic Diagram of 8x1 Multiplexer

## Slide 21: 16x1 MULTIPLEXER USING 8X1 MUX

## Slide 22: Demultiplexers
A demultiplexer has
  N control inputs
  1 data input
  2N outputs
A demultiplexer routes (or connects) the data input to the selected output.
  The value of the control inputs determines the output that is selected.
A demultiplexer performs the opposite function of a multiplexer.

## Slide 23: Demultiplexers
A | B | W | X | Y | Z
0 | 0 | I | 0 | 0 | 0
0 | 1 | 0 | I | 0 | 0
1 | 0 | 0 | 0 | I | 0
1 | 1 | 0 | 0 | 0 | I
W = A'.B'.I
X = A.B'.I
Y = A'.B.I
Z = A.B.I
Out0
In
S1
S0
I
W
X
Y
Z
A
B
Out1
Out2
Out3

## Slide 24: Designing logic circuits using multiplexers
using an n-input Multiplexer
Use an n-input multiplexer to realize a logic circuit for a function with n minterms.
  m = 2n, where m = # of variables in the function
Each minterm of the function can be mapped to an input of the multiplexer.
For each row in the truth table, for the function, where the output is 1, set the corresponding input of the multiplexer to 1.
  That is, for each minterm in the minterm expansion of the function, set the corresponding input of the multiplexer to 1.
Set the remaining inputs of the multiplexer to 0.

## Slide 25: Designing logic circuits using multiplexers
Using an (n / 2)-input Multiplexer
Use an (n / 2)-input multiplexer to realize a logic circuit for a function with n minterms.
  m = 2n, where m = # of variables in the function
Group the rows of the truth table, for the function, into (n / 2) pairs of rows.
  Each pair of rows represents a product term of (m – 1) variables.
  Each pair of rows can be mapped to a multiplexer input.
Determine the logical function of each pair of rows in terms of the mth variable.
  If the mth variable, for example, is x, then the possible values are x, x', 0, and 1.

## Slide 26: Using an (n / 2)-input Mux
Example: F(x,y,z) = Sm(1, 2, 6, 7)

## Slide 27: Using an (n / 2)-input Mux
Example: F(A,B,C,D) = Sm(1,3,4,11,12,13,14,15)

## Slide 28: QUESTIONS:
Design a 16x1 Multiplexer using 2x1 Multiplexer.
Using an 8-to-1 multiplexer, design a logic circuit to realize the following Boolean function F(A,B,C) = Sm(2, 3, 5, 6, 7)
Using an 4-to-1 multiplexer, design a logic circuit to realize the following Boolean function F(A,B,C) = Sm(0,1, 3, 5, 6, 7)
Design a 4 bit Prime number detector.
Design a BCD to Gray Code Converter.

## Slide 29: THANK YOU