## Slide 1: SWITCHING THEORY AND LOGIC DESIGN
UNIT-4
BY
S.SAGAR KRISHNA,
ASSISTANT PROFESSOR,
GAYATRI VIDYA PARISHAD COLLEG OF ENGINEERIN(A)

## Slide 2: PARALLEL IN SERIAL OUT SHIFT REGISTER
In this type, the bits are entered in parallel i.e., simultaneously into their respective stages on parallel lines.
There are four data input lines, X0, X1, X2 and X3 for entering data in parallel into the register.
SHIFT/ LOAD input is the control input, which allows four bits of data to load in parallel into the register.
When SHIFT/LOAD is LOW, gates G1, G2, G3 and G4 are enabled, allowing each data bit to be applied to the D input of its respective Flip-Flop. When a clock pulse is applied, the Flip-Flops with D = 1 will set and those with D = 0 will reset, thereby storing all four bits simultaneously.

## Slide 3: PARALLEL IN SERIAL OUT SHIFT REGISTER
When SHIFT/LOAD is HIGH, gates G1, G2, G3 and G4 are disabled and gates G5, G6 and G7 are enabled, allowing the data bits to shift right from one stage to the next. The OR gates allow either the normal shifting operation or the parallel data entry operation, depending on which AND gates are enabled by the level on the SHIFT/LOAD input.
Parallel-In Parallel-Out Shift Register:

## Slide 4: BI-DIRECTIONAL SHIFT REGISTER
Here data can be shifted either left or right.
A HIGH on the RIGHT/LEFT control input allows data bits inside the register to be shifted to the right, and a LOW enables data bits inside the register to be shifted to the left. When the RIGHT/LEFT control input is HIGH, gates G1, G2, G3 and G4 are enabled, and the state of the Q output of each Flip-Flop is passed through to the D input of the following Flip-Flop. When a clock pulse occurs, the data bits are shifted one place to the right.
When the RIGHT/LEFT control input is LOW, gates G5, G6, G7 and G8 are enabled, and the Q output of each Flip-Flop is passed through to the D input of the preceding Flip-Flop. When a clock pulse occurs, the data bits are then shifted one place to the left.

## Slide 5: COUNTER

## Slide 6: 2 BIT ASYNCHRONOUS COUNTER OR MOD-4 UP COUNTER
If working not clear view this video
https://www.youtube.com/watch?v=iaIu5SYmWVM&list=PLuYnCh-Sh1Xd5cLa-CfK883tPmJwrjSwF

## Slide 7: ASYNCHRONOUS MOD-4 DOWN COUNTER

## Slide 8: DESIGN PROCEDURE ASYNCHRONOUS COUNTER
Each Flip-Flop will give 2 states 0 and 1.So N flip-flop will give 2n states
First Determine no of Flip-Flop Required. If it is a 2 bit 2 flip-flop are required.
MOD-n Counter :(If n is a multiple of 2 )then
if Mod-16 counter is written then it has 16 states starting from 0000 to 1111 in binary. or to get 16 states, n has to be 4.
MOD-n Counter :
If n is not a multiple of 2
First identify no of states, then write the state in binary format. Then the maximum state is considered if it is a r bit then r flip flop are required. But r flip-flop will give 2r States. In order to get maximum state use AND gate for active clear or NAND gate for low clear
Ex:MOD-10 counter means it has 10 states starting from 0000 to 1001 in binary since the last state is a 4 bit number 4 flip flop are required. But 4 flip-flops will give output as 16 states. So we design the circuit in such a way at 1010 the flip-flop has to be reset to zero by connecting NAND gate with inputs as Q3,Q1 for low clear.

## Slide 9: MOD-10 ASYNCHRONOUS COUNTER
Logic Diagram
Functional Table here QD=A,QC=B,OB=C,QA=D

## Slide 10: MOD-10 ASYNCHRONOUS COUNTER
Working:
At first clock output will be 0001 then clr=1 as QD=0,QB=0 then the output will change to 0010 at next clock then clr=1 as QD=0,QB=1.This process will continue until output reaches 1001
When output is 1001 clr=1 as QD=1,QB=0 so at next clock output reaches 1010 but immediately clr=0 as QD=1,QB=1 then all the flip-flop will reset to 0000 and then once again count continues
If any doubts view this video
https://www.youtube.com/watch?v=fKVZpupyP_o
Disadvantages: It will take more time for operation as clock is not common for all flip-flops but it is easy to design

## Slide 11: SYNCHRONOUS COUNTER DESIGN PROCEDURE
Advantage: Faster in operation and more components are required
Design Steps:
The given problem is determined with a state diagram.
From the state diagram, obtain the state table.
Assign binary values to each state (Binary Assignment) if the state table contains letter symbols.
Determine the number of Flip-Flops.
Choose the type of Flip-Flop (SR, JK, D, T) to be used.
From the state table, circuit excitation and output tables.
Using K-map or any other simplification method, derive the circuit output functions and the Flip-Flop input functions.
Draw the logic diagram.

## Slide 12: MOD-8 SYNCHRONOUS COUNTER USING T FF
State Diagram
State table along with excitation table

## Slide 13: MOD-8 SYNCHRONOUS COUNTER USING T FF
TA=1 AS ALL ARE 1 OR CAN VERIFY THROUGH K-MAPS

## Slide 14: MOD-8 SYNCHRONOUS COUNTER USING T FF

## Slide 15: MOD-8 SYNCHRONOUS COUNTER USING T FF
draw the State Diagram with 8 states starting from 000 to 111
As last number is 111 3 flip-flops are required
From the State Diagram write the State Table if PS=000 then NS=001
If PS=001 then NS=010 like this write for every state and if PS=111 then NS=000
After that write excitation table using PS,NS
Then obtain Boolean Expressions for Ta, Tb, Tc
Then draw the logic diagram
See this video if you have doubts
https://www.youtube.com/watch?v=6e8oV2blkGs

## Slide 16: MOD-8 SYNCHRONOUS COUNTER USING T FF
draw the State Diagram with 8 states starting from 000 to 111
As last number is 111 3 flip-flops are required
From the State Diagram write the State Table if PS=000 then NS=001
If PS=001 then NS=010 like this write for every state and if PS=111 then NS=000
After that write excitation table using PS,NS
Then obtain Boolean Expressions for Ta, Tb, Tc
Then draw the logic diagram
See this video if you have doubts
https://www.youtube.com/watch?v=6e8oV2blkGs
Design 3 bit up/down Synchronous counter using T Flip-Flops
https://www.youtube.com/watch?v=svFUEJkoeVY

## Slide 17: RING COUNTER
“CLEAR” signal is firstly applied to all the flip-flops together in order to “RESET” their outputs to a logic “0” level and then a “PRESET” pulse is applied to the input of the first flip-flop ( FFA ) before the clock pulses are applied. This then places a single logic “1” value into the circuit of the ring counter.
So on each successive clock pulse, the counter circulates the same data bit between the four flip-flops over and over again around the “ring” every fourth clock cycle.

## Slide 18: FUNCTIONAL TABLE OF RING COUNTER
QA | QB | QC | QD
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
1 | 0 | 0 | 0
AND THE PROCESS CONTINUES FOR EACH CLOCK |  |  | 

## Slide 19: JOHNSON COUNTER OR TWISTED RING COUNTER
In this the inverted output of the last stage flip flop is connected to the input of first flip flop
“CLEAR” signal is firstly applied to all the flip-flops together in order to “RESET” their outputs to a logic “0” level.
Then QD’=1 so at the next clock output will be 1000. As the inverted output Q is connected to the input D this 8-bit pattern continually repeats. For example, “1000”, “1100”, “1110”, “1111”, “0111”, “0011”, “0001”, “0000”

## Slide 20: FUNCTIONAL TABLE OF JOHNSON COUNTER
QA | QB | QC | QD
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 1
0 | 0 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0
Sequence continues |  |  | 

## Slide 21: QUESTIONS:
Design a 4 bit even parity generator
Convert SR Flip-Flop to JK Flip-Flop
Explain the working of Universal Shift Register.
Design a Mod-8 Asynchronous Counter.
Design a Mod-12 Synchronous Counter.

## Slide 22: THANK YOU