## Slide 1: SWITCHING THEORY AND LOGIC DESIGN
UNIT-5
BY
S.SAGAR KRISHNA,
ASSISTANT PROFESSOR,
GAYATRI VIDYA PARISHAD COLLEG OF ENGINEERIN(A)

## Slide 2: FINITE STATE MACHINES
The synchronous or clocked sequential networks are represented by two models.
Moore model: The output depends only on the present state of the Flip-Flops.
Mealy model: The output depends on both the present state of the Flip-Flops and on the inputs.
Moore model: In the Moore model, the outputs are a function of the present state of the Flip-Flops only. The output depends only on present state of Flip-Flops, it appears only after the clock pulse is applied, i.e., it varies in synchronism with the clock input.

## Slide 3: FINITE STATE MACHINES
Mealy model: In the Mealy model, the outputs are functions of both the present state of the Flip-Flops and inputs

## Slide 4: STATE DIAGRAM
It is a pictorial representation of a behavior of a sequential circuit.
In the state diagram, a state is represented by a circle and the transition between states is indicated by directed lines connecting the circles. A directed line connecting a circle with circle with itself indicates that next state is same as present state. The binary number inside each circle identifies the state represented by the circle. The directed lines are labeled with two binary numbers separated by a symbol ‘/’. The input value that causes the state transition is labeled first and the output value during the present state is labeled after the symbol ‘/’.
In case of Moore circuit, the directed lines are labeled with only one binary number representing the state of the input that causes the state transition. The output state is indicated within the circle, below the present state because output state depends only on present state and not on the input.

## Slide 5: STATE TABLE
It represents relationship between input, output and Flip-Flop states. It consists of three sections labeled present state, next state and output. o The present state designates the state of Flip-Flops before the occurrence of a clock pulse, and the output section gives the values of the output variables during the present state. o Both the next state and output sections have two columns representing two possible input conditions: X= 0 and X=1.

## Slide 6: STATE TABLE
In case of Moore circuit, the output section has only one column since output does not depend on input. and X=1.
Successor: A’s 1 successor is c and A’s 0’s successor is A(used in partition technique)
State Equation: It is an algebraic expression that specifies the condition for a Flip-Flop state transition. The Flip-Flops may be of any type and the logic diagram may or may not include combinational circuit gates.
State Reduction: If some states have same Next State and output then this state becomes a redundant state.This state can be removed. This process is known as State Reduction
State Assignment: In this process each state is assigned a binary value

## Slide 7: PARTITION TECHNIQUE
This also helps in reducing no of States
Example:

## Slide 8: PARTITION TECHNIQUE
Reduced State Table:

## Slide 9: DESIGN A CIRCUIT FOR A GIVEN STATE DIAGRAM USING D FLIP-FLOP:
State Table

## Slide 10: DESIGN A CIRCUIT FOR A GIVEN STATE DIAGRAM USING D FLIP-FLOP:

## Slide 11: DESIGN A CIRCUIT FOR A GIVEN STATE DIAGRAM USING D FLIP-FLOP:

## Slide 12: DESIGN A SEQUENCE DETECTOR TO DETECT SEQUENCE 1010 FOR MEALY TYPE
First draw the state diagram to detect the Sequence 1010(consider overlapping).
When the Sequence is completed the output will be 1.
After drawing State diagram the design procedure is same as explained in slides 9 to 11.
First State table, Excitation table, Boolean Expressions, Logic diagram
Here
S0=00
S1=01
S2=10
S3=11
After that repeat the same procedure mentioned in slides 9 to 11

## Slide 13: DESIGN A SEQUENCE DETECTOR TO DETECT SEQUENCE 1010 FOR MEALY TYPE
When S0=0 we have to wait in the same state with output =0 and if S0=1 we move to S1 with output =0
When S1=0 we move to S1 with output =0 and if S0=1 have to wait in the same state with output =0
When S2=0 we move to S0 as the sequence is wasted with output =0 if S2=1 we move to S3 with output =0
When S3=0 we move to S2 as the sequence is completed as it is overlapping and output =1 as sequence is completed and if S3=1 we move to S1 as it is overlapping and output =0
(If you have doubts look into this video design procedure is present here https://www.youtube.com/watch?v=k8xxGSkJUhY for non overlapping and overlapping sequence)
After State Assignment, repeat the same procedure mentioned in slides 9 to 11

## Slide 14: QUESTIONS:
Design a Sequence Detector to detect the sequence 1011 for Mealy type using D-flip-flop.
Design a Binary Serial Adder for Moore Type.
Draw the state diagram of JK Flip-flop
Reduce the following State Table using Partition Technique.

## Slide 15: THANK YOU